## Slide 1: Inverse procedural Street Modelling: from interactive to automatic reconstruction
Phd Defense : Rémi Cura, 2016/09/12
Université Paris-Est
École Doctorale Mathématiques et Sciences et Technologies
de l'Information et de la Communication (MSTIC)
Pr. Christian Heipke (IPI)
Pr. Peter Van Oosterom (TUDelft) Dr. Florent Lafarge (INRIA)
Pr. Gilles Gesquière (LIRIS)
Dr. Julien Perret (IGN)
Dr. Nicolas Paparoditis (IGN)
Dr. Kevin Lyvan (Thales)
Jury:
Notes: Parler du context de la these :
Entreprise/labo
Projet terra mobilita

## Slide 2: Foreword about this presentation
Work : 3 years
Presentation : 45 minutes
 compression problem
  Lossless
  Only a summary, details in the articles/manuscript
Various people here: it may be fast

## Slide 3: Abstract
Procedural Street Modelling

## Slide 4: PLAN
Introduction: Why model streets? (5’)
State of the art: How to model streets? (5’)
StreetGen : Helping humans model streets
  Generating best guess streets (5’)
  Editing streets (in-base) (5’)
Automating the street generation
  Data? point cloud server (5’)
  Fitting the street model (5’)
Conclusion (5’)

## Slide 5: Introduction
Why model streets?
Usages for street model

## Slide 6: 1. Introduction
1.1 Why Model streets ?
  Streets are important:
    Streets are essential parts of cities
    Cities are important places
  Information is important
    Modelling of a street = knowledge about this street
    Used for visualisation / simulation / analysis

## Slide 7: Introduction: Streets are important
Cities are important places
  Many people live in it
    World : 50% in urban area.
    France : 80%
  Concentrate people/power/usages/issues
Streets are important in cities
  In paris, streets area > building area
  Streets = medium between people/occupations

## Slide 8: Introduction: having a model is important
Modelling the streets
  Visualisation (map / 3D model)
  Simulation
  Analysis
  …
Why would we want an accurate, structured, up to date map of streets?
  Mapping = maps are classical control/management tools
    Map war for South America (Madrid, 1750)
  Mapping = visualising: very helpful for human
    (demo th. Pythagore visual vs math)

## Slide 9: Introduction
Why model streets?
Usages for street model

## Slide 10: Introduction: usages for street model
Cities are actually carefully managed
    Paris : 100’ of people, one dedicated engineer school
  Requires data (precise, up to date)
  Visualisation (map / 3D model)
    Decision making
    Consultation / communication
  Simulation
    Traffic / pollution / noise / parkings …
  Analysis (past/present/planning)

## Slide 11: Introduction: usages for city model
Street model ⊂ city model
Many usages for a city model

## Slide 12: State of the art
Modelling street, why is it hard?
Existing models

## Slide 13: State of the art: modelling street is hard
Even ‘regular’ streets are hard to model
  Complex (even for human)
  Traffic
  Organised
  Hard to sense

## Slide 14: State of the art: modelling street is hard
Streets are complex

## Slide 15: State of the art: modelling street is hard
Streets are complex

## Slide 16: State of the art: modelling street is hard
Streets are complex

## Slide 17: State of the art: modelling street is hard
Streets are a medium supporting all type of traffic

## Slide 18: State of the art: modelling street is hard
Streets are organised (symmetry, hierarchy, part of network …)

## Slide 19: State of the art: modelling street is hard
Streets are hard to sense
  Manual : millions of objects
  Automatic :
    high occlusion
    Small details are essential (curb)

## Slide 20: State of the art
Modelling street, why is it hard?
Existing models

## Slide 21: State of the art: Existing models
What should be modelled?
  Street precise geometry (roadway/ sidewalk / …)
  Street road as part of whole network (= traffic info)
  Street organisation
  Street objects
  Street objects relations
  Material/visual aspects …

## Slide 22: State of the art: Existing models
Everybody is interested by different street aspects
  GIS : road as center line + buffer
  Traffic simulation : road network / pedestrian space
  Computer graphics : nice 3D roads blending with surroundings
  Procedural modelling : road network as start for procedural city
  Sensing : mostly road surface and markings
  driving simulator : intersection
  Automotiv industrial : roadway detailed characteristics
  …

## Slide 23: State of the art: Existing models
Everybody is interested by different street aspects
  GIS : road as center line + buffer
  Traffic simulation : road network / pedestrian space
  Computer graphics : nice 3D roads blending with surroundings
  Procedural modelling : road network as start for procedural city
  Sensing : mostly road surface and markings
  driving simulator : intersection
  Automotive industrial : roadway detailed characteristics
  …

## Slide 24: State of the art: Existing models
Serna2015
Boyko2011
Guo2015
Montoya-Zegarra2014
Chen2008
Gallin2011
Kuntzsch2015
Wilkie2012
Despine2011
Wang2015
Road XML
CityGML
Open Drive

## Slide 25: State of the art: Existing models
  Whole system modelling
    City GML : for city, but contains a road module
    Road XML : oriented for traffic simulation
    Open Drive : high geometric details

## Slide 26: State of the art: Existing models
  Data-driven modelling
    From image/lidar
Serna2015
Boyko2011
Guo2015
Classif + Context + CRF
Fitting + active contour
Cascade random forest
Extraction, raster, template matching
Montoya-Zegarra2014

## Slide 27: State of the art: Existing models
  GIS-based modelling
Kuntzsch2015
Wilkie2012
Street segment KDE, intersection with RJ-MCMC
Turning radius, network of lane, simulation

## Slide 28: State of the art: Existing models
  Simulation-based modelling
Despine2011
Wang2015
Network from data, guessing lane, intersection by continuity, 3D generation
Segment of road parametrisation, intersection…

## Slide 29: State of the art: Existing models
  Procedural modelling
Chen2008
Gallin2011
Tensor, stream line, grammar
Terrain, graph : shortest path and merging, procedural generation

## Slide 30: StreetGen : generate streets
Design Principle
Kinematic hypothesis
Road surface
Traffic support
Street objects

## Slide 31: StreetGen : design principle
  To Design = to compromise
  Goals?
    Model streets of whole Paris (scale, robustness)
    Work with limited GIS data (best guess)
    Model used for various outputs (analysis/ 3D visu / traffic simulation...)
    Multi-user editing
  Our approach:
    Limited data : based on road axis, use simple kinematic hypothesis
    Scaling & multi-user : use a RDBMS
    Coherent structured model : use a RDBMS

## Slide 32: StreetGen : design principle
Not a model for all streets, but a model for most of streets
3 observations on streets
  Structured by street axis
  2 type of parts : morphologically constant or variying
  Adapted to vehicle traffic
Kinematic hypothesis :
  Allows to rough out a road model
Scaling/multi-user/GIS data  use a RDBMS

## Slide 33: StreetGen : generate streets
StreetGen : graphical abstract

## Slide 34: StreetGen : design principle
  StreetGen road model

## Slide 35: StreetGen : design principle
How to deal with several users? Use a RDBMS !
Road modeling
Read file , process, write results in a file
RDBMS : made to abstract & secure data
  UPDATE MODELING (SYNC)
user
user
user
user
user
StreetGen
Ask computing on/ edit
Visualize
User input
Input data

## Slide 36: StreetGen : design principle
Need 1-neighboorhood to compute a street
May be computed simultaneously

## Slide 37: StreetGen : generate streets
Design Principle
Kinematic hypothesis
Road surface
Traffic support
Street objects

## Slide 38: StreetGen : Kinematic hypothesis
Hypothesis
  road border is defined by a vehicle driving along it at a given speed, while making comfortable turns.
  Street type  vehicle speed
  Vehicle speed  turning radius
  Turning radius  road surface

## Slide 39: StreetGen : Kinematic hypothesis
  Illustrations :
3m
9m
~ Road type

~ speed

~ radius
width
Or some actual speed database

## Slide 40: StreetGen : Kinematic hypothesis
  Various radius in Paris

## Slide 41: StreetGen : Kinematic hypothesis
We have road axis, road width
  How to compute circle center and arcs?
  analytical computing (vector, angle) ?

## Slide 42: StreetGen : Kinematic hypothesis
t

## Slide 43: StreetGen : generate streets
Design Principle
Kinematic hypothesis
Road surface
Traffic support
Street objects

## Slide 44: StreetGen : Road surface
Find intersection limit :
  Project circle centers
  Farthest per axis
1
1
2,3
4
5

## Slide 45: StreetGen : Road surface
Intersection surface :
  By geometric operation

## Slide 46: StreetGen : Road surface
Special intersection:
Variable buffer

## Slide 47: StreetGen : Road surface
results

## Slide 48: StreetGen : generate streets
Design Principle
Kinematic hypothesis
Road surface
Traffic support
Street objects

## Slide 49: StreetGen : Traffic Support
For traffic simulation:
  Lanes
  Possible trajectories in interconnections.
A real traffic simulation requires much more
  Average speed
  Type of intersection (roundabout/traffic light)
  Etc …
But : without further information, we do what we can!

## Slide 50: StreetGen : Traffic Support
Lane ased on road axis : but not translation

## Slide 51: StreetGen : Traffic Support
Intersection trajectory : Bezier curves:
  Not accurate (kinematically), but easy to create and edit
  Involves center of intersection in special cases

## Slide 52: StreetGen : generate streets
Design Principle
Kinematic hypothesis
Road surface
Traffic support
Street objects

## Slide 53: StreetGen : street objects
Streets objects : incredibly varied
  13k references on ArchiExpo
  Markings : 1k pages of norms
  …
  Objects are in relation (hierarchical, spatial, semantic …)
  Not many common points between all kind of street objects
    Street objects are often spatially organized relatively to the street axis

## Slide 54: StreetGen : street objects
So we use generic objects
  Positioned/oriented relatively to street axis

## Slide 55: StreetGen : street objects
Objects are points with semantic
DBMS can support any relation (hierarchy, semantic…)

## Slide 56: StreetGen : street objects
Also can also be surface (or polylines?) :
Pedestrian crossing for instance

## Slide 57: StreetGen : street objects
Whole Paris in 10 min.
Tested for simulation (SimuVia)
Tested for 3D visu (Thales DBMaker)
Tested to model other cities (Mali)
Tested to model airport runway

## Slide 58: StreetGen : street objects
Of course, lot of limitations
Street model:
  Not enough for some street
  Radius seems to be historical rather than related to speed
Technical
  Technical glitches/bugs
  Precision issues
Traffic
  All possible interconnection : too much
Objects
  Lack linear objects

## Slide 59: StreetGen : editing streets (in-base)
In-base interaction Principle
Edit road model
Edit traffic
Edit objects

## Slide 60: StreetGen : street objects
How to edit street model easily (several concurrent users) ?

## Slide 61: StreetGen : street objects
Fact : developing a Graphical User Interface (GUI) is hard, long and risky (maintenance)
Many GUI for many tools (web/desktop/…)
  Need to create plugins/interfaces/…
Idea : use existing tools
  GIS tools can already edit vector and attributes
  specific interactions are in base

## Slide 62: StreetGen : street objects
example:
In GIS software
In base

## Slide 63: StreetGen : street objects
In-base interaction are generic and powerful
  Extensively uses triggers
  Several design patterns
    Help create interactions
    Help manage user input

## Slide 64: StreetGen : street objects
All StreetGen street model can be edited concurrently
  Road axis/ width
  Radius
  Lane
  Interconnection
  objects

## Slide 65: StreetGen : street objects
Multi-user editing can be facilitated
“Interactive Map Tracking” QGIS plugin with Lionel Atty

## Slide 66: StreetGen : street objects
Results:
  Interaction are fast enough to be interactive
Video
https://youtu.be/fQZoEfUcNHA

## Slide 67: StreetGen : street objects
Several Limitations
  In-base interaction should be limited to straightforward interaction (guessing user action is easy)
  Hard to develop/test/maintain (no modern signal feature)
  All interaction happen in one transaction  should be short
  Topological network editing is limited (ill-posed problem)
  Initial building of topology is slow
  More information needed for traffic simulation
  Objects:
    relative to absolute positioning is not a bijection

## Slide 68: Automating street modelling
Inverse procedural modelling
Data: Point Cloud Server
Fitting model to real streets

## Slide 69: StreetGen : Inverse procedural modelling
Fit a generic procedural model to a specific situation
Specific situation?
 We need data!
Simon2011
Talton2011

## Slide 70: Abstract
Procedural Street Modelling

## Slide 71: Abstract
Inverse
Procedural Street Modelling

## Slide 72: StreetGen : Inverse procedural modelling
What type of data for streets?
  Precise
  Good coverage
  Frequent
Aerial image?
 Too far!

## Slide 73: StreetGen : Inverse procedural modelling
IGN dedicated mobile mapping: Stereopolis
  Cameras
  Lidar

## Slide 74: StreetGen : Inverse procedural modelling
Street view:
  Good coverage

## Slide 75: StreetGen : Inverse procedural modelling
Lidar: 3D point clouds
  precise 3D

## Slide 76: Automating street modelling
Inverse procedural modelling
Data: Point Cloud Server
Fitting model to real streets

## Slide 77: Point Cloud Server
Point Cloud Server : manage massive amounts of geospatial point clouds in a database.
Many type of geospatial point clouds
Aerial LIDAR
Terrestrial LIDAR
Medical
imaging
Stereovision

## Slide 78: Point Cloud Server: Problems
Problem:
  Massive data  need
    Sharing
    Filtering
    Efficient I/O
    Compression
  Very specific for various purposes
    (many tools/formats/usage)
  Point cloud != only processing
    need to manage the entire pipeline
    need meta data / contextual information
    cross use with other data

## Slide 79: Point Cloud Server: State of the art
File-based
  Simple, no concurrency
  Can’t do much with points
DBMS (point storing)
  Powerfull
  Can’t scale
NoSQL
  Scale well
  Specific and tailored
Cloud
  Ultimate scaling
  Theoretical problem with indexing
DBMS (group of points storing)
  All inclusive
  Points need to be group-able
Managing billions of nD-points : difficult !
Managing millions of groups of points: easy!
≠
Otepka et al., 2013
Rieg et al., 2014
van Oosterom et al., 2015
Greyhound

## Slide 80: Point Cloud Server: Method
Idea:
PCS = a … server !
Many interfaces
possible
Abstraction
safe
RDBMS
File system
Point Cloud Server

## Slide 81: Point Cloud Server: Method
Workflow

## Slide 82: Point Cloud Server: Method
Main idea about storing
GPS_time (s) X (m) Y(m) Z(m) reflectance (…. )
54160.295 2068.230 20690.025 45.934 -9.4497 (…. )
1 point =
1 row = 1 point
Analogy : Pixels
1 row = N points
Analogy : Image
Usage : do we really need to get points 1 by 1?
Billions points
Million groups
Color = group

## Slide 83: Point Cloud Server: Loading/Exporting
Loading/exporting points into the PCS:
  2 flavors : how much does the server work?

## Slide 84: Point Cloud Server: Loading/Exporting
Paris
Terrestrial lidar
2.15 B points
750 ply files
42 linear km
21 attributes
Typical resolution: 1 cm

## Slide 85: Point Cloud Server: Loading/Exporting
Paris loading speed: 75k pts/s writing : 200k pts/s
  Not far from actual sensing speed
  Could be faster (Vanoosterom2015)
We load point clouds, but how are they stored?

## Slide 86: Point Cloud Server: generalisation
Group of points (aka patch) generalisation
  Generalisation = abstraction

## Slide 87: Point Cloud Server: generalisation
Other generalisation
  Essential : abstracting the data = more abstract usage
  Ex : points within flat neighborhood vertical VS points in a wall
Top view in QGIS

## Slide 88: Point Cloud Server: processing
More generalisation

## Slide 89: Point Cloud Server: filtering
With so much data:
  Essential to access only a part of it : example
Patches that are
  far from buildings
  close to the intersection these 2 streets
  aerial view color ≈ pedestrian crossing
  close trajectory
  with high point density

## Slide 90: Point Cloud Server: filtering
Result : finding millions of points amongst billions :
  100 ms if indexed !
?
points
Points in patch
Which points are inside the polygon?
Get points in these patches
Which patchs are inside the polygon?
Which points are inside the polygon?

## Slide 91: Point Cloud Server: processing
Postgresql: easy to add in-base processing
  C/Cpp  for performance
  R/Python  for fast prototyping
Example :
  Verticality descriptor
  Unsupervised clustering
  Plane & cylinder detection

## Slide 92: Point Cloud Server: processing
Converting patch to raster
  Cornerstone detection
  Marking detection
  Façade detection

## Slide 93: Point Cloud Server: processing
classification

## Slide 94: Point Cloud Server: processing
Patches can be used in a graph structure

## Slide 95: Point Cloud Server: Level Of Detail
Level Of Detail (LOD):
  Sometimes you don’t need all the points
  12 Millions points, really?
  User need only a given level of detail.

## Slide 96: Point Cloud Server: Level Of Detail
Idea : implicit LOD
  order the point by importance
  Reading the points gradually increases the level of detail

## Slide 97: Point Cloud Server: Level Of Detail
Example

## Slide 98: Point Cloud Server: Level Of Detail
Example

## Slide 99: Point Cloud Server: Level Of Detail
For visualization, LOD depends on distance to camera

## Slide 100: Point Cloud Server: Level Of Detail
LOD enables point streaming
Mettre screen paul blottiere

## Slide 101: Point Cloud Server: Level Of Detail
Also for classical GIS soft that can’t deal with too many points

## Slide 102: Point Cloud Server: Level Of Detail
Limitations
  Points have to be group-able
  Our Loading/export could be much faster
  Filtering is fast at patch level(O(ln(n))), not point level (O(n))
  LOD : rely on ordering the points !
    You have to use it
    May be slow to build
    For the moment, getting a part of the patch require to read it entirely

## Slide 103: Automating street modelling
Inverse procedural modelling
Data: Point Cloud Server
Fitting model to real streets

## Slide 104: Inverse Procedural modelling: method
Initial road model + observation  optimisation  fit road model

## Slide 105: Inverse Procedural modelling: method
Initial road model + observation  match observation to axis optimisation  fit road model

## Slide 106: Inverse Procedural modelling: observations
Observation = clues about roadway

## Slide 107: Inverse Procedural modelling: observations
Observation = clues about roadway

## Slide 108: Inverse Procedural modelling: forces
Observations generate forces on road axis/width
Each street object type has an expected position:
  IN/OUT + BORDER_IN/BORDER_OUT (dist)
Ex :
  road markings : IN
  Pedestrian crossing marking : BORDER_IN (0.2 m)
  Traffic sign : OUT
  No parking markings : BORDER_OUT (0.1m)

## Slide 109: Inverse Procedural modelling: forces
Each type of street object expected position is defined in a table

## Slide 110: Inverse Procedural modelling: forces
Observations generate forces on road axis/width
Each street object type has an expected position:
  IN/OUT + BORDER_IN/BORDER_OUT + dist

## Slide 111: Inverse Procedural modelling: forces
So if we sum up forces from observations :

## Slide 112: Inverse Procedural modelling: forces
Others forces: resisting changes : express confidence in initial road model

## Slide 113: Inverse Procedural modelling : matching
Observations generate force on road axis/width, But first :
Observation matching road axis:
Closest road surface

## Slide 114: Inverse Procedural modelling: matching
In intersection : can’t use observations:
  We would need to optimise full road surface model

## Slide 115: Inverse Procedural modelling: experiment
Optimisation = Non-linear least square
   no guarantee to find the optimal solution, robust, very fast
Open source : Ceres solver
Areas of experiment:

## Slide 116: Inverse Procedural modelling : small area

## Slide 117: Inverse Procedural modelling : small area

## Slide 118: Inverse Procedural modelling : small area

## Slide 119: Inverse Procedural modelling : small area

## Slide 120: Inverse Procedural modelling : small area

## Slide 121: Inverse Procedural modelling : small area
Quantitative evaluation:
Only kerb observation:
  Median dist to sidewalk : from 1.8m  0.4m
Kerb observation + user input
  Median dist to sidewalk : from 1.8m  0.34m
It’s much better in a challenging area!

## Slide 122: Inverse Procedural modelling : sensing area
Whole sensing area:
Results:

## Slide 123: Inverse Procedural modelling : sensing area
Yellow circle are proportional to error:
Most of the cases :
  Not enough curb detection!
Sometime:
  Road model not sufficient
Seldom:
  Optimisation not optimal

## Slide 124: Inverse Procedural modelling : sensing area
Quantitative evaluation:
Only kerb observation:
  Median dist to sidewalk : from 1.5m  0.6m
Many streets in the area lack kerb observations, but still significantly better.

## Slide 125: Inverse Procedural modelling : Paris area
Whole Paris : topology is broken at fews points

## Slide 126: Inverse Procedural modelling: Paris area
Quantitative evaluation:
Using ground truth as observation
  Median dist to sidewalk : from 1.5m  0.1m
still residuals, why?

## Slide 127: Inverse Procedural modelling: error sources
Residual sources

## Slide 128: Inverse Procedural modelling: Streetgen on optim
Once simple road model is optimised, we can generate streets with StreetGen

## Slide 129: Inverse Procedural modelling: Streetgen on optim
Streetgen after optimisation

## Slide 130: Inverse Procedural modelling: Streetgen on optim
Traffic information is generated (but has not been optimised)

## Slide 131: Inverse Procedural modelling: Limitations
(Many) Limitations
  Road model is too simple
  Constant number of parameters in optim
  For the moment, objects are almost useless
  Must choose between trusting initial model and trusting observations
  How to deal with parking places?

## Slide 132: Conclusion
Summary
Limitations
Perspectives

## Slide 133: Conclusion: Summary
From low information: generate best guess street model at Paris scale and edit it (multi-user, many GIS software): StreetGen

## Slide 134: Conclusion: Summary
Manage a massive amount of 3D points (from mobile mapping). Act as a service for usage/processing/visu.

## Slide 135: Conclusion: Summary
Perform inverse procedural modelling by fitting a road model to various observations

## Slide 136: Conclusion
Summary
Limitations
Perspectives

## Slide 137: Conclusion: Limitations
Very simple street model: revolves around street axis.
  Too simple?
  Pedestrian street?
  Based on topology  hard to maintain/scale/edit
Objects are created/edited manually by user
  Tedious, not much sense
  They should be created by template/ pattern/ grammar/procedural functions!
Point Cloud Server :
  Need several processing methods to extract observations
Optimisation : going meta

## Slide 138: Conclusion
Summary
Limitations
Perspectives

## Slide 139: Conclusion: Perspectives
Only the beginning of inverse procedural street modelling.
  Dealing with objects and road model simultaneously calls for much stronger modelling and optimisation methods
Since the beginning of the thesis :
  Major trend in smart vehicle/autonomous cars
  maps no more required only by traditional data provider
   maps potentially required by every (Billion) cars
Many work about smart city
  Time is essential (simulation/understanding)
  4D street modelling ? (garbage/ café terrace/ parking behaviour)
Understanding city may be key to planning study city history

## Slide 140: Conclusion: Perspectives
Jacoubet, 1810-1836 :
road model with optimisation & Streetgen ?

## Slide 141: Conclusion: Perspectives
Turgot, 1734-1739 : procedural modelling candidate?

## Slide 142: QUESTIONS
Thanks
Questions?

## Slide 143: TODO
Finish layout for optim
  Use it in optim and in conclusion part
Last “question” slide with streetgen
Conclusion need illustrations and splitting slides